## Slide 3
In the circuit of Figure 1, Va = +3 V, Vb = +4 V, Vc = +5 V, Ra = Rb = Rc= 3 kΩ, RF = 1 kΩ, ROM = 270 Ω, and supply voltages = ± 15 V. Assuming that the op-amp is initially nulled, determine the output voltage Vo.
-2 V
-3 V
-4 V
-5 V

## Slide 4
Answer : C

## Slide 5
In the circuit of Figure 1, Va = 200 mV, Vb = -300 mV, Vc = 400 mV, Ra = 3 kΩ, Rb = 2.2 kΩ,Rc= 1 kΩ, RF = 4.7 kΩ, ROM = 470 Ω and RL = 10 kΩ, and supply voltages = ± 15 V. (i) Determine the output voltage Vo.
-0.55 V
-1.55 V
-2.55 V
-3.55 V

## Slide 6
Solution: (i)Vo = -[RF/Ra (Va) + RF/Rb (Vb) + RF/Rc (Vc)]
= -[(4.7/3)(200) + (4.7/2.2)(-300) + (4.7/1)(400)]
= -[313.33 – 640.90 + 1880]
= -1552.43 mV = -1.552 V = -1.552 V
Answer : B

## Slide 7
In the circuit of Figure 1, Va = 150 mV, Vb = -350 mV, Vc = 450 mV, Ra = 3 kΩ, Rb = 2.2 kΩ,Rc= 1 kΩ, RF = 4.7 kΩ, ROM = 470 Ω and RL = 10 kΩ, and supply voltages = ± 15 V. (i) Determine the output voltage Vo.
-1.602 V
-2.602 V
-4.602 V
-5.602 V

## Slide 8
Solution: (i)Vo = -[RF/Ra (Va) + RF/Rb (Vb) + RF/Rc (Vc)]
=-[(4.7/3)(150) + (4.7/2.2)(-350) + (4.7/1)(450)]
= -[235 – 747.72 + 2115]
= -1602.28 mV = -1.602 V = -1.602 V
Answer : A

## Slide 11
In the circuit of Figure 2, Va = +3 V, Vb = -3 V, Vc = +3 V, R = R1 = 1 kΩ, RF = 2 kΩ. Determine the voltage V1 at the non-inverting terminal. Assuming that the op-amp is initially nulled.
0.1 V
1.0 V
0.2 V
2.0 V

## Slide 12
Solution: (i)V1 = [Va + Vb + Vc]/3
= [3 + (-3) + 3]/3
= 1.0 V
Answer : B

## Slide 13
In the circuit of Figure 2, Va = +5 V, Vb = -5 V, Vc = +9 V, R = R1 = 1 kΩ, RF = 2 kΩ. Determine the output voltage Vo. Assuming that the op-amp is initially nulled.
7 V
8 V
9 V
10 V

## Slide 14
Solution: (i)V1 = [Va + Vb + Vc]/3
= [5 + (-5) + 9]/3
= 3.0 V
Vo = (1+RF/R1)V1 = (1+2) 3 = 9 V
Answer : C

## Slide 15
In the circuit of Figure 2, Va = +5 V, Vb = -5 V, Vc = +9 V, R = R1 = 1 kΩ, RF = 3 kΩ. Determine the output voltage Vo. Assuming that the op-amp is initially nulled.
12 V
13 V
14 V
15 V

## Slide 16
Solution: (i)V1 = [Va + Vb + Vc]/3
= [5 + (-5) + 9]/3
= 3.0 V
Vo = (1+RF/R1)V1 = (1+3) 3 = 12 V
Answer : A

## Slide 19
In the circuit of Figure 2, R = 1 kΩ, Va = +9 V, Vb = +5 V, Vc = +5 V, Vd = +6 V. Determine the output voltage Vo.
1 V
2 V
3 V
4 V

## Slide 20
Answer : C

## Slide 23
In the circuit of Figure 1, Vin = 5 V, R = 20 kΩ, and V1 = 2 V. Find the load current.
0.05 mA
0.10 mA
0.15 mA
0.25 mA

## Slide 24
Solution: IL = Vin / R
= 5 /(20 x 103)
= 0.25 mA
Answer : D

## Slide 25
In the circuit of Figure 1, Vin = 5 V, R = 20 kΩ, and V1 = 2 V. Find the output voltage Vo.
4 V
5 V
6 V
7 V

## Slide 26
Solution: V0 = 2V1
= 2 x 2
= 4 V
Answer : A

## Slide 27
Q. Calculate Q for a wide bandpass filter with fL = 250 Hz, fH = 25 kHz.
0.101
0.202
0.303
0.404

## Slide 28
Solution: fC = [fLfH]1/2
= [250 x 25000]1/2
= 2500 Hz
Q = fC/(fH-fL) = 2500/(25000-250) = 0.101
Answer: A