## Slide 3
Q. Calculate the effective resistance R’L seen looking into the primary of a 25:1 transformer ratio connected to an output load of 8Ω.

## Slide 4
Solution: Given N1 = 25 , N2 = 1 , n = N2/N1
= [N1/N2]2RL
= [25]2 x 8
= 625 x 8 = 5000 Ω
= 5 k Ω

## Slide 11
Q. Class A power amplifier has a transformer as the load. If the transformer has a turns ratio of 5 and the secondary load is 100 Ω, determine the maximum ac power output. Given that zero signal collector current is 100 mA.

## Slide 12
Solution: Given N1 : N2 = 5 , and n = N2/N1
= [N1/N2]2RL
= [5]2 x 100
= 25 x 100 = 2500 Ω

## Slide 13
Therefore, maximum ac power output,
= (½)(100 x 10-3)2 x 2500
= (½) x 25
= 12.5 W