## Slide 1
Q.1. For a given op-amp, CMRR = 105 and differential gain Ad = 105. Determine the common-mode gain Acm of the op-amp.

## Slide 2
Solution: Given CMRR = 105, Ad = 105
therefore, Acm = 105/105 = 1

## Slide 3
For a given op-amp, the common mode rejection ration (CMRR) is given as
Acm/Ad
Ad/Acm
Acm + Ad
Ad - Acm

## Slide 4
Q.2. For a given op-amp, common-mode gain Acm = 0.5 and differential gain Ad = 105. Determine the common-mode rejection ration (CMRR).

## Slide 5
Answer: 2 x 105

## Slide 6
Q.3. The output voltage of a certain op-amp circuit changes by 20 V in 4 µs. What is its slew rate?

## Slide 7
Solution: Given dVo = 20 V, dt = 4 µs
therefore, Slew Rate = 20/4 = 5 V/µs

## Slide 8
For a given op-amp, the slew rate is given as
dt/dVo
dt + dVo
dVo + dt
dVo/dt

## Slide 9
Q.4. The slew rate of a certain op-amp circuit is 4 V/µs. What is the change in output voltage for this slew rate if change in output voltage occurs in 4 µs.

## Slide 10
Answer: 16 V

## Slide 11
Q.5. Determine the output voltage in the following case for the open-loop differential amplifier :
(a) vin1 = 5 µV dc, vin2 = -7 µV dc
The op-amp has open loop gain A = 200000.
Solution: Given vin1 = 5 µV dc, vin2 = -7 µV dc , A = 200000
therefore, vo = 200000 [5 x 10-6 - (-7 x 10-6)] = 2.4 V dc

## Slide 12
Q.6. Determine the output voltage in the following case for the open-loop differential amplifier :
(a) vin1 = 10 mV , vin2 = 20 mV
The op-amp has open loop gain A = 200000.

## Slide 13
Solution: Given vin1 = 10 mV, vin2 = 20 mV , A = 200000
therefore, vo = 200000 [10 x 10-3 - (20 x 10-3)]
= -2000 V

## Slide 14
The output voltage of an op-amp connected in inverting amplifier configuration is given as

## Slide 15
Q.7. Determine the output voltage for the inverting amplifier if :
vin = 20 mV dc
The op-amp has open loop gain A = 200000.
Solution: Given vin = 20 mV dc, A = 200000
therefore, vo = -200000 [20 x 10-3 ] = -4000 V dc

## Slide 16
The output voltage of an op-amp working as non-inverting amplifier configuration is given as

## Slide 17
Q.8. Determine the output voltage for the non-inverting amplifier if :
vin = 25 µV dc
The op-amp has open loop gain A = 200000.
Solution: Given vin = 25 µV dc, A = 200000
therefore, vo = 200000 [25 x 10-6 ] = 5 V dc

## Slide 18
For an op-amp connected in non-inverting amplifier configuration with feedback, the closed loop gain is given as,

## Slide 19
Q.9. An op-amp having the following parameters is connected as a non-inverting amplifier with feedback:
A = 200000, R1 = 1 kΩ, RF = 10 kΩ
Calculate the values of AF.
Solution: Given A = 200000, R1 = 1 kΩ, RF = 10 kΩ
therefore, B = 1/1+10 = 1/11

## Slide 20
therefore, AF = 200000/[1+(200000 x 1/11)]
= 10.99