## Slide 1: ISO (International Organization for Standardization)
Till No……
ISO 9000
ISO 9001
ISO 14001
Environmental Performance Criteria

## Slide 2: Which of the following provides the standard for environment quality management:
ISO 9000
ISO 9001
ISO 14000
ISO 22000

## Slide 3: Environmental performance criteria

## Slide 4: Environmental Performance Criteria
https://www.youtube.com/watch?v=F3SUC72DD5I&ab_channel=MashitahDrahim

## Slide 5: Environmental performance criteria
for
desktop personal computers,
notebook personal computers and
personal computer monitors
IEEE Standard 1680
Section 4
It summarizes the content of the standard needed by a manufacturer to assess or declare a product’s conformance with the Standard

## Slide 6: Contents
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging

## Slide 7
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Reduction/elimination of environmentally sensitive materials | 
Reduction of use of hazardous substances | All covered products shall comply with the final requirements of the European RoHS Directive 2002/95/EC for the restriction on certain hazardous substances in electronic equipment. The Directive addresses cadmium, mercury, lead, hexavalent chromium, and certain brominated flame retardants.
Cadmium | 
Elimination of Intentionally added cadmium | Concentrations of cadmium shall be less than half the threshold defined in RoHS, unless the presence of cadmium can be shown to be due to use of recycled content.
Reporting on amount of mercury used in light sources | For all flat panel video display devices manufacturers shall report on the amount of mercury used in light sources in all covered products. Low threshold for amount of mercury used in light sources.

## Slide 8
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Elimination of intentionally added lead in certain applications | Video display units shall have concentrations of lead less than 5 percent of the threshold defined in the RoHS Directive per listed part, unless the presence of lead can be shown to be due to use of recycled content
Elimination of intentionally added hexavalent chromium | shall have concentrations of hexavalent chromium that are less than half the threshold defined in the RoHS Directive, unless the presence of hexavalent chromium can be shown to be due to use of recycled content.
Flame retardants and plasticizers | Shall contain no more than a trace amount of Short Chain Chlorinated Paraffin (SCCPs) in paints, coatings, plastics, rubbers or seals, unless the presence of SCCPs can be shown to be due to use of recycled content. Plastic parts larger than 25 grams shall contain no more than a trace amount of the flame retardants classified as dangerous substances under the European Directive on the classification, packaging and labeling of dangerous substances.

## Slide 9
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Batteries free of lead, cadmium and mercury | As per European Directive 91/157/EEC on batteries and accumulators containing certain dangerous substances products shall not contain lead, cadmium and mercury over trace amounts.
Large plastic parts free of polyvinyl chloride | In all covered products, except cables and interconnect parts, parts greater than 25 grams shall not contain polyvinyl chloride (PVC).

## Slide 10
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Total recycled plastics content | For all covered products that contain plastics, except printed circuit boards and packaging, manufacturers shall Declare whether plastic parts include greater than 5 percent recycled resins. Contain an average of at least 10 percent postconsumer recycled plastic. Shall contain an average of at least 25 percent (higher content) postconsumer recycled plastic.
Renewable/biobased plastic materials | For all plastic parts, except packaging, manufacturer Shall declare whether product contains greater than 5 percent renewable/biobased plastic materials Shall contain an average of at least 10 percent renewable or biobased plastic
Declaration of product weight (Dematerialization) | For all covered products, except packaging, manufacturer shall declare the product weight.

## Slide 11
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Design for recovery through recycling systems that utilize shredding | 
Manufacturer shall provide treatment information to reuse and recycling facilities | 
Elimination of paints or coatings that are not compatible with recycling or reuse | products shall not contain paints and coatings on larger plastic parts that are not compatible with recycling and reuse.
Easy disassembly of external enclosure | products shall have enclosures that are easily removable
Marking of plastic components | All larger plastic components shall be marked with a resin identification code according to the international (ISO) standard
Identification and removal of components containing hazardous materials. | All covered products shall have larger circuit boards, and other components that contain hazardous materials, safely and easily identifiable and removable

## Slide 12
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Design for recovery through recycling systems that utilize shredding | 
Reduced number of plastic material types | The enclosures for all covered products shall have all the larger parts composed of only one type of plastic.
Molded/glued in metal eliminated or removable | Shall not contain molded-in or glued-in metal inserts in plastic enclosures unless they are easy to remove
Easy disassembly of external enclosure | Products shall have enclosures that are easily removable
Minimum 65 percent reusable/recyclable | Products shall have at least 65 percent of the materials in the product reusable or recyclable using current infrastructure and technologies
Minimum 90 percent reusable/recyclable | Products shall have at least 90 percent of the materials in the product reusable or recyclable using current infrastructure and technologies.
Design for recovery through disassembly | Products shall have the plastic parts, except very small ones, easily separable Products shall have the plastic components, except very small ones, marked with a resin identification code according to the international (ISO) standard

## Slide 13
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Product longevity / life cycle extension | 
Manufacturer warranty/service agreement | additional three year warranty or service agreement available for purchase
Upgradeability | 
Upgradeable with common tools | All computers shall be upgradeable with common tools, including memory drives, chips and cards that can be changed or extended
Modular design | modular design such that major components and processor can be changed.
Product life extension | Spare or replacement parts shall be available for five years as well as information on how to obtain the parts

## Slide 14
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Energy conservation | 
Power management system | Shall comply with the version of U.S. ENERGY STAR that is applicable at the time of declaration. If an ENERGY STAR specification is modified, presently registered products shall have six months to update their declaration to the new version shall qualify and be certified to a new ENERGY STAR specification in advance of its effective date.
Use of renewable energy | 
 | Shall have a commercially available accessory for powering the product that uses renewable energy
 | Shall be shipped with a standard component for powering the product that allows for the use of renewable energy.

## Slide 15
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
End of life management | 
Product take-back | Shall include the option to purchase, at a competitive price, a take-back or recycling service that meets the U.S. EPA environmental standard defined in the “Plug-In to eCycling Guidelines for Materials Management,” published May 2004. Shall include an annual audit, according to the “Plug-In to eCycling Guidelines,” of all first, second and third tier recycling facilities that are used to provide the services required in above criterion.
Rechargeable battery recycling | shall include the option to purchase, at a competitive price, a rechargeable, lithium-ion battery take-back service that is equivalent to or better than that provided by the Rechargeable Battery Recycling Corporation (RBRC).

## Slide 16
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Corporate performance | 
Corporate environmental policy | shall demonstrate the existence and public availability of a written corporate environmental policy consistent with ISO 14001
Environmental management system | All organizations shall have Self-certified environmental management system for design and manufacturing facilities.
 | Third-party certified environmental management system for design and manufacturing facilities ISO 14001, European EMAS or U.S. EPA Performance Track
Corporate Reporting | Corporate report consistent with Performance Track or Global Reporting Initiative. Corporate report based on Global Reporting Initiative (GRI)

## Slide 17
Reduction/elimination of environmentally sensitive materials
Materials selection
Design for end of life
Product longevity / life cycle extension
Energy conservation
End of life management
Corporate performance
Packaging
Packaging | 
Toxics in packaging | Heavy metals shall not be intentionally added to any packaging or packaging component, with an exception for the use recycled content
Recyclable packaging materials | shall have all non-reusable packaging separable into like materials without using tools.
Recycled Content | The manufacturer shall declare whether packaging contains recycled content, or does not, and shall declare the approximate recycled content for each material.
Take-Back Option | Provision of take-back program for packaging
Reuse Option | Manufacturer shall provide at a competitive price a reusable packaging process that reuses the packaging for a minimum of five reuses for the same or similar product.