## Slide 1: Control Engineering

## Slide 2
Elements of Modelling

## Slide 3: Physical Systems
Physical systems can be classified into various types:
  Electrical systems
  Mechanical systems
Electronic systems
Hydraulic systems
Thermal systems
Each of these systems can be modelled in terms of certain basic
elements
Basic elements of all physical systems can be shown to be analogous
3

## Slide 4: Electrical Systems
4
Based on the type of source, electrical systems can be classified as:
  Voltage sourced systems
  Current sourced systems
Voltage sourced | Current sourced
Basic System Elements | 
Resistor (𝑅) | Resistor (𝑅)
Inductor (𝐿) | Inductor (𝐿)
Capacitor (𝐶) | Capacitor (𝐶)
Basic System Variables | 
Voltage (𝑉) | Current (𝐼)
Charge (𝑄) | Flux (𝜙)

## Slide 5: Electrical System Elements
Resistor (𝑅): It is an element which resists the flow of current in an
electrical system
𝑉 = 𝐼𝑅
Inductor (𝐿): It is an element that stores electrical energy in a magnetic field
𝑑𝜙 𝑑𝐼
𝑉 = 𝑑𝑡 = 𝐿 𝑑𝑡
Capacitor (𝐶): It is an element that stores electrical energy in a electrical field
𝑑𝑞 𝑑𝑉
𝐼 = 𝑑𝑡 = 𝐶 𝑑𝑡
Anuj
:
𝑅
𝐿
𝐶
5

## Slide 6: Mechanical Systems
Classification based on type of motion:
  Translational systems having linear motion
  Rotational systems having angular motion about a fixed axis
Anuj
Translational | Rotational
Basic System Elements | 
Mass (𝑀) | Inertia (𝐽)
Damper (𝐵) | Damper (𝐷)
Linear spring (𝐾) | Torsional spring (𝐾)
Basic System Variables | 
Force (𝐹) | Torque (𝑇)
Displacement (𝑥) | Angular displacement (𝜃)
11

## Slide 7: Mass Vs Inertia
Mass
Property of an element that stores the kinetic energy due to translational motion
When a force is acting on a body of mass 𝑀 causing displacement 𝑥, then:
𝐹 = 𝑑𝑃 = 𝑀 𝑑2 𝑥 = 𝑀𝑥
𝑑𝑡 𝑑𝑡2
Inertia
Property of an element that stores the kinetic energy due to rotational motion
When a torque is acting on a body of inertia J causing displacement 𝜃, then:
𝑑2 𝜃
:
𝐹
𝑥
𝑀
𝑇 = 𝐽 = 𝐽𝜃
𝑑𝑡2
𝑇
𝜃
𝐽
12

## Slide 8: Damper
𝑑𝑡
𝑑𝑥
𝐹 = 𝐵 = 𝐵𝑥
𝑑𝜃
𝑇 = 𝐷 𝑑𝑡 = 𝐷𝜃
Damper is an element that generates force which acts opposite to the direction of motion, translational or rotational
Damper resists motion
Friction or dashpot are examples of dampers
Translational Rotational
𝐹
𝑥
𝐵
𝑇
𝜃
:
Photos Courtesy
Note: R&C represent ports
𝐷

## Slide 9: Linear Vs Torsional Spring
Linear Spring
Property of an element that stores the potential energy due to translational motion
When a spring of spring constant
𝐾 is applied a force 𝐹 causing an elastic displacement 𝑥, then:
𝐹 = 𝐾𝑥
𝐹
𝑥
𝐾
Torsional spring
Property of an element that stores the potential energy due to rotational motion
When a torsional spring of constant
𝐾 is applied a torque 𝑇 causing an angular displacement 𝜃, then:
𝑇 = 𝐾𝜃
𝑇
𝜃
𝐾
:
Noe: R&C represent ports

## Slide 10: Nodal Analysis for Mechanical Systems
System structure should be modified to suit nodal analysis, without loss of system characteristics
Steps of nodal analysis are detailed by an example
Anuj
15

## Slide 15: Nodal Analysis : Example
Node 1
Reference
𝑀
𝐾2
𝐵
𝐾1
Node 2
Step 1:
Number of nodes = 2
Hence, number of displacements = 2
𝐹
:
Photos Courtesy

## Slide 16: Nodal Analysis : Example
𝑥1
Reference Node
𝑥2
Step 2:
Displacement and reference nodes are
identified
:

## Slide 17: Nodal Analysis : Example
𝑥2
Reference Node
Step 3:
Connect mass 𝑀 between
node 𝑥2 and reference node
Step 4:
Connect spring 𝐾1 between
nodes 𝑥1 and 𝑥2
Connect spring 𝐾2 between
𝑥2 and reference node
Step 5:
Connect the force 𝐹 between 𝑥1 and reference node
𝑥1
𝐹
𝐵
𝐾1
𝐾2
𝑀
:

## Slide 18: Nodal Analysis : Example
Step 6:
Apply Newton’s 2nd law at node 𝑥1:
𝐹 = 𝐾1 𝑥1 − 𝑥2 (1)
Apply Newton’s 2nd law at node 𝑥2:
2 2 1 2 1
0 = 𝑀𝑥 + 𝐵𝑥 + 𝐾 𝑥 − 𝑥 +
2 2
𝐾 𝑥 (2)
Eq.1 and Eq.2 give the mathematical model of the given mechanical system
𝑥2
Reference Node
𝑥
1
𝐹
:
𝐵
𝐾1
𝐾2
𝑀

## Slide 21: Summary: Steps of Nodal Analysis
Identify number of nodes which is equal to number of displacements
Take a reference node independent of other nodes (displacement nodes)
Connect all mass / inertia elements between the relevant displacement node and the reference node irrespective of its position
Connect spring and damper elements between relevant nodes based on their position
Connect force or torque between the relevant displacement node and the reference node
At each of the displacement nodes, apply Newton’s laws of motion

## Slide 22: Analogous Systems
Mechanical systems can be represented using electrical elements
by the following analogies
Two types of analogies:
  Force (Torque) - Voltage analogy (F-V analogy)
    Force is analogous to voltage
  Force (Torque) - Current Analogy (F-I analogy)
    Force is analogous to current

## Slide 29: Summary: Analogous Systems
Following table shows the analogue between the elements of mechanical and electrical systems:
Anuj
Mechanical System |  | Electrical System | 
Translational | Rotational | F-V Analogy | F-I Analogy
Force (𝐹) | Torque (𝑇) | Voltage (𝑉) | Current (𝐼)
Mass (𝑀) | Inertia (𝐽) | Inductor (𝐿) | Capacitor (𝐶)
Friction (𝐵) | Friction (𝐷) | Resistor (𝑅) | Conductor (1/𝑅)
Linear spring (𝐾) | Torsional spring (𝐾) | Capacitor (1/𝐶) | Inductor (1/𝐿)
Displacement (𝑥) | Displacement (𝜃) | Charge (𝑞) | Flux (𝜙)
25

## Slide 40
If a pole is located at s = -5 in left-hand plane (LHP), how will it be represented in Laplace domain?
a. 1/ s + 5 b. 1/ s – 5 c. s/ s + 5 d. s/ s – 5

## Slide 41
ANSWER: (a) 1/ s + 5