## Slide 1: INSTRUCTION SET OF 8085

## Slide 2: Instruction Set of 8085
An instruction is a binary pattern designed inside a microprocessor
to perform a specific function.
The entire group of instructions that a microprocessor supports is called Instruction Set.
8085 has 246 instructions.
Each instruction is represented by an 8-bit binary value.
These 8-bits of binary value is called Op-Code or Instruction Byte.

## Slide 3: Classification of Instruction Set
Data Transfer Instruction
Arithmetic Instructions
Logical Instructions
Branching Instructions
Control Instructions

## Slide 4: Data Transfer Instructions
These instructions move data between registers, or between
memory and registers.
These instructions copy data from source to destination.
While copying, the contents of source are not modified.

## Slide 5: Data Transfer Instructions
Opcode | Operand | Description
MOV | Rd, Rs Rd, M M, Rs | Copy from source to destination.
This instruction copies the contents of the source register into the
destination register.
The contents of the source register are not altered.
If one of the operands is a memory location, its location is specified by
the contents of the HL registers.
Example: MOV B, C
MOV B, M
MOV M, C

## Slide 6: Data Transfer Instructions
Opcode | Operand | Description
MVI | Rd, Data M, Data | Move immediate 8-bit
The 8-bit data is stored in the destination register or memory.
If the operand is a memory location, its location is specified by the contents of the H-L registers.
Example: MVI A, 57H
MVI M, 57H

## Slide 7: Data Transfer Instructions
Opcode | Operand | Description
LXI | Reg. pair, 16-bit data | Load register pair immediate
This instruction loads 16-bit data in the register pair.
Example: LXI H, 2034 H

## Slide 8: Data Transfer Instructions
Opcode | Operand | Description
LDA | 16-bit address | Load Accumulator
The contents of a memory location, specified by a 16- bit address in the operand, are copied to the accumulator.
The contents of the source are not altered.
Example: LDA 2034H

## Slide 9: Data Transfer Instructions
Opcode | Operand | Description
LDAX | B/D Register Pair | Load accumulator indirect
The contents of the designated register pair point to a memory location.
This instruction copies the contents of that memory location into the accumulator.
The contents of either the register pair or the memory location are not altered.
Example: LDAX B

## Slide 10: Data Transfer Instructions
Opcode | Operand | Description
LHLD | 16-bit address | Load H-L registers direct
This instruction copies the contents of memory location pointed out by 16-bit address into register L.
It copies the contents of next memory location into register H.
Example: LHLD 2040 H

## Slide 11: Data Transfer Instructions
Opcode | Operand | Description
STA | 16-bit address | Store accumulator direct
The contents of accumulator are copied into the memory location specified by the operand.
Example: STA 2500 H

## Slide 12: Data Transfer Instructions
Opcode | Operand | Description
STAX | Reg. pair | Store accumulator indirect
The contents of accumulator are copied into the memory location specified by the contents of the register pair.
Example: STAX B

## Slide 13: Data Transfer Instructions
Opcode | Operand | Description
SHLD | 16-bit address | Store H-L registers direct
The contents of register L are stored into memory location specified by the 16-bit address.
The contents of register H are stored into the next memory location.
Example: SHLD 2550 H

## Slide 14: Data Transfer Instructions
Opcode | Operand | Description
XCHG | None | Exchange H-L with D-E
The contents of register H are exchanged with the contents of register D.
The contents of register L are exchanged with the contents of register E.
Example: XCHG

## Slide 15: Arithmetic Instructions
These instructions perform the operations like:
  Addition
  Subtract
  Increment
  Decrement

## Slide 16: Addition
Any 8-bit number, or the contents of register, or the contents of
memory location can be added to the contents of accumulator.
The result (sum) is stored in the accumulator.
No two other 8-bit registers can be added directly.
Example: The contents of register B cannot be added directly to the
contents of register C.

## Slide 17: Subtraction
Any 8-bit number, or the contents of register, or the contents of memory location can be subtracted from the contents of accumulator.
The result is stored in the accumulator.
Subtraction is performed in 2’s complement form.
If the result is negative, it is stored in 2’s complement form.
No two other 8-bit registers can be subtracted directly.

## Slide 18: Increment / Decrement
The 8-bit contents of a register or a memory location can be
incremented or decremented by 1.
The 16-bit contents of a register pair can be incremented or decremented by 1.
Increment or decrement can be performed on any register or a
memory location.

## Slide 19: Arithmetic Instructions
Opcode | Operand | Description
ADD | R M | Add register or memory to accumulator
The contents of register or memory are added to the contents of
accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of the addition.
Example: ADD B or ADD M

## Slide 20: Arithmetic Instructions
Opcode | Operand | Description
ADC | R M | Add register or memory to accumulator with carry
The contents of register or memory and Carry Flag (CY) are added to the
contents of accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of the addition.
Example: ADC B or ADC M

## Slide 21: Arithmetic Instructions
Opcode | Operand | Description
ADI | 8-bit data | Add immediate to accumulator
The 8-bit data is added to the contents of accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of the addition.
Example: ADI 45 H

## Slide 22: Arithmetic Instructions
Opcode | Operand | Description
ACI | 8-bit data | Add immediate to accumulator with carry
The 8-bit data and the Carry Flag (CY) are added to the contents of accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of the addition.
Example: ACI 45 H

## Slide 23: Arithmetic Instructions
Opcode | Operand | Description
DAD | Reg. pair | Add register pair to H-L pair
The 16-bit contents of the register pair are added to the contents of H-L pair.
The result is stored in H-L pair.
If the result is larger than 16 bits, then CY is set.
No other flags are changed.
Example: DAD B

## Slide 24: Arithmetic Instructions
Opcode | Operand | Description
SUB | R M | Subtract register or memory from accumulator
The contents of the register or memory location are subtracted from the
contents of the accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of subtraction.
Example: SUB B or SUB M

## Slide 25: Arithmetic Instructions
Opcode | Operand | Description
SBB | R M | Subtract register or memory from accumulator with borrow
The contents of the register or memory location and Borrow Flag (i.e. CY)
are subtracted from the contents of the accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of subtraction.
Example: SBB B or SBB M

## Slide 26: Arithmetic Instructions
Opcode | Operand | Description
SUI | 8-bit data | Subtract immediate from accumulator
The 8-bit data is subtracted from the contents of the accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of subtraction.
Example: SUI 45 H

## Slide 27: Arithmetic Instructions
Opcode | Operand | Description
SBI | 8-bit data | Subtract immediate from accumulator with borrow
The 8-bit data and the Borrow Flag (i.e. CY) is subtracted from the contents of the accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of subtraction.
Example: SBI 45 H

## Slide 28: Arithmetic Instructions
Opcode | Operand | Description
INR | R M | Increment register or memory by 1
The contents of register or memory location are incremented by 1.
The result is stored in the same place.
If the operand is a memory location, its address is specified by
the contents of H-L pair.
Example: INR B or INR M

## Slide 29: Arithmetic Instructions
Opcode | Operand | Description
INX | R | Increment register pair by 1
The contents of register pair are incremented by 1.
The result is stored in the same place.
Example: INX H

## Slide 30: Arithmetic Instructions
Opcode | Operand | Description
DCR | R M | Decrement register or memory by 1
The contents of register or memory location are decremented by 1.
The result is stored in the same place.
If the operand is a memory location, its address is specified by
the contents of H-L pair.
Example: DCR B or DCR M

## Slide 31: Arithmetic Instructions
Opcode | Operand | Description
DCX | R | Decrement register pair by 1
The contents of register pair are decremented by 1.
The result is stored in the same place.
Example: DCX H

## Slide 32: Logical Instructions
These instructions perform logical operations on data stored in registers, memory and status flags.
The logical operations are:
  AND
  OR
  XOR
  Rotate
  Compare
  Complement

## Slide 33: AND, OR, XOR
Any 8-bit data, or the contents of register, or memory location can logically have
  AND operation
  OR operation
  XOR operation
with the contents of accumulator.
The result is stored in accumulator.

## Slide 34: Rotate
Each bit in the accumulator can be shifted either left or right to the next position.

## Slide 35: Compare
Any 8-bit data, or the contents of register, or memory location can be compares for:
  Equality
  Greater Than
  Less Than
with the contents of accumulator.
The result is reflected in status flags.

## Slide 36: Complement
The contents of accumulator can be complemented.
Each 0 is replaced by 1 and each 1 is replaced by 0.

## Slide 37: Logical Instructions
Opcode | Operand | Description
CMP | R M | Compare register or memory with accumulator
The contents of the operand (register or memory) are compared with the contents of the accumulator.
Both contents are preserved .
The result of the comparison is shown by setting the flags of the PSW as follows:

## Slide 38: Logical Instructions
Opcode | Operand | Description
CMP | R M | Compare register or memory with accumulator
if (A) < (reg/mem): carry flag is set
if (A) = (reg/mem): zero flag is set
if (A) > (reg/mem): carry and zero flags are reset.
Example: CMP B or CMP M

## Slide 39: Logical Instructions
Opcode | Operand | Description
CPI | 8-bit data | Compare immediate with accumulator
The 8-bit data is compared with the contents of accumulator.
The values being compared remain unchanged.
The result of the comparison is shown by setting the flags of the PSW as follows:

## Slide 40: Logical Instructions
Opcode | Operand | Description
CPI | 8-bit data | Compare immediate with accumulator
if (A) < data: carry flag is set
if (A) = data: zero flag is set
if (A) > data: carry and zero flags are reset
Example: CPI 89H

## Slide 41: Logical Instructions
Opcode | Operand | Description
ANA | R M | Logical AND register or memory with accumulator
The contents of the accumulator are logically ANDed with the contents of
register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result of the operation.
CY is reset and AC is set.
Example: ANA B or ANA M.

## Slide 42: Logical Instructions
Opcode | Operand | Description
ANI | 8-bit data | Logical AND immediate with accumulator
The contents of the accumulator are logically ANDed with the 8-bit data.
The result is placed in the accumulator.
S, Z, P are modified to reflect the result.
CY is reset, AC is set.
Example: ANI 86H.

## Slide 43: Logical Instructions
Opcode | Operand | Description
XRA | R M | Exclusive OR register or memory with accumulator
The contents of the accumulator are XORed with the contents of the register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result of the operation.
CY and AC are reset.
Example: XRA B or XRA M.

## Slide 44: Logical Instructions
Opcode | Operand | Description
ORA | R M | Logical OR register or memory with accumulator
The contents of the accumulator are logically ORed with the contents of the register or
memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: ORA B or ORA M.

## Slide 45: Logical Instructions
Opcode | Operand | Description
ORI | 8-bit data | Logical OR immediate with accumulator
The contents of the accumulator are logically ORed with the 8- bit data.
The result is placed in the accumulator.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: ORI 86H.

## Slide 46: Logical Instructions
Opcode | Operand | Description
XRA | R M | Logical XOR register or memory with accumulator
The contents of the accumulator are XORed with the contents of the
register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result of the operation.
CY and AC are reset.
Example: XRA B or XRA M.

## Slide 47: Logical Instructions
Opcode | Operand | Description
XRI | 8-bit data | XOR immediate with accumulator
The contents of the accumulator are XORed with the 8-bit data.
The result is placed in the accumulator.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: XRI 86H.

## Slide 48: Logical Instructions
Opcode | Operand | Description
RLC | None | Rotate accumulator left
Each binary bit of the accumulator is rotated left by one position.
Bit D7 is placed in the position of D0 as well as in the Carry
flag.
CY is modified according to bit D7.
S, Z, P, AC are not affected.
Example: RLC.

## Slide 49: Logical Instructions
Opcode | Operand | Description
RRC | None | Rotate accumulator right
Each binary bit of the accumulator is rotated right by one position.
Bit D0 is placed in the position of D7 as well as in the Carry
flag.
CY is modified according to bit D0.
S, Z, P, AC are not affected.
Example: RRC.

## Slide 50: Logical Instructions
Opcode | Operand | Description
RAL | None | Rotate accumulator left through carry
Each binary bit of the accumulator is rotated left by one position through the Carry flag.
Bit D7 is placed in the Carry flag, and the Carry flag is placed in
the least significant position D0.
CY is modified according to bit D7.
S, Z, P, AC are not affected.
Example: RAL.

## Slide 51: Logical Instructions
Opcode | Operand | Description
RAR | None | Rotate accumulator right through carry
Each binary bit of the accumulator is rotated right by one position through the Carry flag.
Bit D0 is placed in the Carry flag, and the Carry flag is placed in
the most significant position D7.
CY is modified according to bit D0.
S, Z, P, AC are not affected.
Example: RAR.

## Slide 52: Logical Instructions
Opcode | Operand | Description
CMA | None | Complement accumulator
The contents of the accumulator are complemented.
No flags are affected.
Example: CMA.

## Slide 53: Logical Instructions
Opcode | Operand | Description
CMC | None | Complement carry
The Carry flag is complemented.
No other flags are affected.
Example: CMC.

## Slide 54: Logical Instructions
Opcode | Operand | Description
STC | None | Set carry
The Carry flag is set to 1.
No other flags are affected.
Example: STC.

## Slide 55: Branching Instructions
The branching instruction alter the normal sequential flow.
These instructions alter either unconditionally or conditionally.

## Slide 56: Branching Instructions
Opcode | Operand | Description
JMP | 16-bit address | Jump unconditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand.
Example: JMP 2034 H.

## Slide 57: Branching Instructions
Opcode | Operand | Description
Jx | 16-bit address | Jump conditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand based on the specified flag of the PSW.
Example: JZ 2034 H.

## Slide 58: Jump Conditionally
Opcode | Description | Status Flags
JC | Jump if Carry | CY = 1
JNC | Jump if No Carry | CY = 0
JP | Jump if Positive | S = 0
JM | Jump if Minus | S = 1
JZ | Jump if Zero | Z = 1
JNZ | Jump if No Zero | Z = 0
JPE | Jump if Parity Even | P = 1
JPO | Jump if Parity Odd | P = 0

## Slide 59: Branching Instructions
Opcode | Operand | Description
CALL | 16-bit address | Call unconditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand.
Before the transfer, the address of the next instruction after CALL (the contents of the program counter) is pushed onto the stack.
Example: CALL 2034 H.

## Slide 60: Branching Instructions
Opcode | Operand | Description
Cx | 16-bit address | Call conditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand based on the specified flag of the PSW.
Before the transfer, the address of the next instruction after the call (the contents of the program counter) is pushed onto the stack.
Example: CZ 2034 H.

## Slide 61: Call Conditionally
Opcode | Description | Status Flags
CC | Call if Carry | CY = 1
CNC | Call if No Carry | CY = 0
CP | Call if Positive | S = 0
CM | Call if Minus | S = 1
CZ | Call if Zero | Z = 1
CNZ | Call if No Zero | Z = 0
CPE | Call if Parity Even | P = 1
CPO | Call if Parity Odd | P = 0

## Slide 62: Branching Instructions
Opcode | Operand | Description
RET | None | Return unconditionally
The program sequence is transferred from the subroutine to the calling program.
The two bytes from the top of the stack are copied into the program counter, and program execution begins at the new address.
Example: RET.

## Slide 63: Branching Instructions
Opcode | Operand | Description
Rx | None | Call conditionally
The program sequence is transferred from the subroutine to the calling program based on the specified flag of the PSW.
The two bytes from the top of the stack are copied into the program counter, and program execution begins at the new address.
Example: RZ.

## Slide 64: Return Conditionally
Opcode | Description | Status Flags
RC | Return if Carry | CY = 1
RNC | Return if No Carry | CY = 0
RP | Return if Positive | S = 0
RM | Return if Minus | S = 1
RZ | Return if Zero | Z = 1
RNZ | Return if No Zero | Z = 0
RPE | Return if Parity Even | P = 1
RPO | Return if Parity Odd | P = 0

## Slide 65: Branching Instructions
Opcode | Operand | Description
RST | 0 – 7 | Restart (Software Interrupts)
The RST instruction jumps the control to one of eight memory locations depending upon the number.
These are used as software instructions in a program to transfer program execution to one of the eight locations.
Example: RST 3.

## Slide 66: Restart Address Table
Instructions | Restart Address
RST 0 | 0000 H
RST 1 | 0008 H
RST 2 | 0010 H
RST 3 | 0018 H
RST 4 | 0020 H
RST 5 | 0028 H
RST 6 | 0030 H
RST 7 | 0038 H

## Slide 67: Control Instructions
The control instructions control the operation of microprocessor.

## Slide 68: Control Instructions
Opcode | Operand | Description
NOP | None | No operation
No operation is performed.
The instruction is fetched and decoded but no operation is executed.
Example: NOP

## Slide 69: Control Instructions
Opcode | Operand | Description
HLT | None | Halt
The CPU finishes executing the current instruction and halts any further execution.
An interrupt or reset is necessary to exit from the halt state.
Example: HLT

## Slide 70: Control Instructions
Opcode | Operand | Description
DI | None | Disable interrupt
The interrupt enable flip-flop is reset and all the interrupts except the TRAP are disabled.
No flags are affected.
Example: DI

## Slide 71: Control Instructions
Opcode | Operand | Description
EI | None | Enable interrupt
The interrupt enable flip-flop is set and all interrupts are enabled.
No flags are affected.
This instruction is necessary to re-enable the interrupts (except TRAP).
Example: EI

## Slide 72: Control Instructions
Opcode | Operand | Description
RIM | None | Read Interrupt Mask
This is a multipurpose instruction used to read the status of interrupts 7.5, 6.5, 5.5 and read serial data input bit.
The instruction loads eight bits in the accumulator with the following interpretations.
Example: RIM

## Slide 73: RIM Instruction

## Slide 74: Control Instructions
Opcode | Operand | Description
SIM | None | Set Interrupt Mask
This is a multipurpose instruction and used to implement the 8085 interrupts 7.5, 6.5, 5.5, and serial data output.
The instruction interprets the accumulator contents as follows.
Example: SIM

## Slide 75: SIM Instruction