## Slide 2
In the circuit of Figure 1, R1 = 260 Ω, R2 = 60 kΩ. The op-amp is 741 with supply voltages = ± 15 V. Determine the lower threshold voltage Vlt.

## Slide 3
Answer: -64.7 mV

## Slide 4
In the circuit of Figure 1, R1 = 260 Ω, R2 = 60 kΩ. The op-amp is 741 with supply voltages = ± 15 V. Determine the upper threshold voltage Vut.

## Slide 5
Answer: 64.7 mV

## Slide 8
In the circuit of Figure 1, determine the size of each step if RF = 1.2 kΩ.

## Slide 9
Answer: -0.6 V

## Slide 10
In the circuit of Figure 1, if RF = 1.2 kΩ, what is the output voltage when inputs b0 through b3 are at 5 V?

## Slide 11
Answer: -9.0 V

## Slide 14
In the circuit of Figure 3, determine the size of each step if RF = 27 kΩ.

## Slide 15
Answer: -0.84375 V

## Slide 16
In the circuit of Figure 3, if RF = 27 kΩ, what is the output voltage when inputs b0 through b3 are at 5 V?

## Slide 17
Answer: -12.66 V