## Slide 1
Q1. An RC coupled amplifier has a voltage gain of 1000, f1 = 50 Hz, f2 = 200 kHz, and a distortion of 5%, without feedback. Find the amplifier voltage gain, f1f, f2f, and distortion (Df) when a negative feedback is applied with feedback ratio of 0.01.

## Slide 2
Q1. An RC coupled amplifier has a voltage gain of 1000, f1 = 50 Hz, f2 = 200 kHz, and a distortion of 5%, without feedback. Find the amplifier voltage gain, f1f, f2f, and distortion (Df) when a negative feedback is applied with feedback ratio of 0.01.
Solution: Since negative feedback is applied, and given
A = 1000, β = 0.01, D = 5%, f1 = 50 Hz, f2 = 200KHz
= 1000/(1+1000x0.01)
= 1000/(1+10) = 1000/11
= 90.90

## Slide 3
New lower 3 dB frequency,
= 50 / (1+1000x0.01)
= 50 / (1+10)
= 4.5 Hz
Similarly, New upper 3 dB frequency,
)
= 200 x 103(1+1000x0.01)
= 200 x 103(1+10)
= 2200 x 103 Hz
= 2.2 x 106 Hz = 2.2 MHz
= 2200 KHz

## Slide 4
Since negative feedback is applied,
= 0.05/(1+1000x0.01)
= 0.0045
= 0.45%

## Slide 5
Q2. The open-loop voltage gain of an amplifier is 50. Its input impedance is 1 kΩ. What will be the input impedance where a negative feedback of 10% is applied to the amplifier?

## Slide 6
Q2. The open-loop voltage gain of an amplifier is 50. Its input impedance is 1 kΩ. What will be the input impedance where a negative feedback of 10% is applied to the amplifier?
Solution: Since negative feedback is applied, and given
A = 50, β = 0.1, Ri = 1 kΩ
)
= 1 x 103(1+50x0.1)
= 1 x 103(1+5) = 1000 x 6 Ω
= 6000 Ω = 6 kΩ

## Slide 7
Q3. The open-loop voltage gain of an amplifier is 50. Its output impedance is 40 kΩ. When a negative feedback is applied, the output impedance becomes 6.666 kΩ. Find the feedback factor.

## Slide 8
Q3. The open-loop voltage gain of an amplifier is 50. Its output impedance is 40 kΩ. When a negative feedback is applied, the output impedance becomes 6.666 kΩ. Find the feedback factor.
Solution: Since negative feedback is applied, and given
A = 50, Ro = 40 kΩ, Rof = 6.666 kΩ
)
6.666 = 40 / (1+50 )
(1+50 ) = 40 / 6.666
(1+50 ) = 6
50 = 6-1 = 5
= 5/50 = 0.1

## Slide 9
Q4. The distortion in an amplifier is found to be 3% when the feedback ratio of a negative feedback amplifier is 0.04. When the feedback is removed, the distortion becomes 15%. Find the open-loop gain and closed loop gain.

## Slide 10
Q4. The distortion in an amplifier is found to be 3% when the feedback ratio of a negative feedback amplifier is 0.04. When the feedback is removed, the distortion becomes 15%. Find the open-loop gain and closed loop gain.
Solution: D = 15% = 0.15, Df = 3% = 0.03, = 0.04
)
0.03 = 0.15 / (1+ x 0.04 )
(1+ x 0.04 ) = 0.15 / 0.03 = 5
(A x 0.04) = 5-1 = 4
A = 4/0.04 = 100

## Slide 11
= 100 / (1 + 100 x 0.04)
= 100 / 1+4
= 100 /5 = 20

## Slide 12
Q5. If negative feedback with a feedback factor of 0.01 is introduced into an amplifier with a gain of 200 and a bandwidth of 6 MHz, obtain the resulting bandwidth of the feedback amplifier.

## Slide 13
Q5. If negative feedback with a feedback factor of 0.01 is introduced into an amplifier with a gain of 200 and a bandwidth of 6 MHz, obtain the resulting bandwidth of the feedback amplifier.
Solution: A = 200, BW = 6 MHz, = 0.01
)
= 6 x 106 (1+ 200 x 0.01 )
= 6 x 106 (1+ 2)
= 18 x 106
= 18 MHz

## Slide 14
Q6. If non linear distortion in a negative feedback amplifier with an open-loop gain of 100 is reduced from 40% to 10%. Find the of the amplifier.

## Slide 15
Q6. If non linear distortion in a negative feedback amplifier with an open-loop gain of 100 is reduced from 40% to 10%. Find the of the amplifier.
Solution: A = 100, Df = 0.1, D = 0.4
)
0.1 = 0.4 / (1+ 100 x β)
(1+100 x β ) = 0.4 /0.1 = 4
(100 x β) = 4-1 = 3
β = 3/100 = 0.03